## Slide 1: Design & Analysis of Majority Logic based Approximate Adders & Multipliers
IIIT Bangalore
Group 13
April 11, 2023

## Slide 2: Agenda
01. Introduction
02. Synopsis
03. Implementation
04. Epilogue
05. References

## Slide 3: INTRODUCTION

## Slide 4: Approximate Computing
Approximate computing is a computing paradigm that aims to provide efficient and low-power solutions to computational problems by relaxing the requirement for exact computation and allowing for some degree of error or imprecision in the results. The basic idea behind approximate computing is to trade-off accuracy for efficiency, by accepting some level of error or inexactness in exchange for gains in speed, power consumption, or other performance metrics.
Why approximation?
  Approximation becomes necessary when exact computation is too expensive, time-consuming, or impossible to achieve.
  In many real-world applications, exact computation may require too many resources or be impractical due to limitations in the available technology, the amount of data to be processed, or the complexity of the problem being solved.
  Approximate methods offer a flexible and efficient approach to addressing such challenges, by providing a range of trade-offs between accuracy and performance, depending on the specific requirements of the problem being solved.
  Approximate computing has been used in a variety of domains where the applications are error-tolerant, such as multimedia processing, machine learning, signal processing, scientific computing. Therefore, approximate computing is mostly driven by applications that are related to human perception/cognition and have inherent error resilience.
How to accomplish?
  Hardware: Approximate circuits, Voltage scaling, Storages and Systems
  Software: Reduced-precision arithmetic, Approximate algorithm, Code optimization

## Slide 5: Aim
The paper proposes the following designs:
  A new 2-bit MLAFA (Majority Logic Approximate Full Adder) is proposed based on truth table reduction; it can be used for multi-bit approximate adder design;
  A 2 x 2 MLAM (Majority Logic Approximate Multiplier) is proposed and complement bits are introduced;
  A novel analysis for selecting complement bits is presented;
  MLACs (Majority Logic Approximate Compressors) based on K-Map simplification and 1-bit MLAFAs are proposed;
  Exact as well as approximate pipelined reduction circuits for 4 x 4 and 8 x 8 MLAMs are proposed.

## Slide 6: SYNOPSIS

## Slide 7: Majority Logic
Majority logic is a type of digital logic that operates on a set of input signals and produces an output signal based on the majority of the input signals.
In majority logic, the output signal is determined by counting the number of input signals that are asserted (i.e., have a logic level of 1) and comparing it to a threshold value.
If the number of asserted signals is greater than or equal to the threshold value, the output signal is asserted; otherwise, the output signal is negated (i.e., has a logic level of 0).
A majority gate is a logical gate used in circuit complexity and other applications of Boolean circuits. A majority gate returns true if and only if more than 50% of its inputs are true.
From Table 1, we can write:
F = M(A, B, C) = AB + BC + AC
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Table 1 : Truth table of Majority gate

## Slide 8
Why majority logic ?
As CMOS is approaching its technology limitations, emerging nanotechnologies have been proposed at the end of the Moore’s Law, such as Quantum-dot Cellular Automata (QCA), nanomagnetic logic (NML), and spin-wave devices (SWD). All of these technologies rely on majority logic (ML) as digital design framework; this is different from conventional Boolean logic.
Figure 1 : Majority gate schematic
Figure 2 : Majority gate cell view

## Slide 9: Error Metrics
As approximate computing introduces errors, metrics are required to evaluate the accuracy of approximate circuits. This paper evaluate approximate designs by the Normalized Mean Error Distance (NMED), and the Maximum Absolute Error (MAE).
The NMED is the normalizing Mean Error Distance. The Mean Error Distance is defined as the average of the Error Distance (ED) which is the absolute difference between the approximate and the accurate results across all possible inputs. MAE is defined as the maximum absolute error.
The definitions of ED, MED, NMED, and MAE are as follows:
ED = |(ExR – ApR)|
MED = (∑ ED) / N
NMED = MED / MAX
MAE = max{ED},
where ExR, ApR, N and MAX denote the accurate result, the approximate result, the counts of all possible inputs and the maximum value of the result, respectively.

## Slide 10: IMPLEMENTATION (I. Approximate Adder)

## Slide 11: 1 – Bit MLAFA
A 1 – bit MLAFA has been proposed in [1]. In the paper it is named as MLAFA1.
From Table 2, the equations for the carry out and the sum are as follows:
Cout = M(A, B, Cin)
S = ~Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
Figure 3 : MLAFA1 schematic diagram
Table 2 : MLAFA1 truth table
[1] C. Labrado, H. Thapliyal and F. Lombardi, "Design of majority logic based approximate arithmetic circuits," 2017 IEEE International Symposium on Circuits and Systems (ISCAS), Baltimore, MD, USA, 2017, pp. 1-4, doi: 10.1109/ISCAS.2017.8050819.

## Slide 12
Proposed 1 – bit MLAFA
A new1 – bit MLAFA, namely MLAFA2 is proposed. The equations for the carry out and the sum are as follows:
Cout = Cin
S = M(~Cout, M(A, B, ~Cin), Cin) = M(A, B, ~Cin)
The MED and NMED of MLAFA2 are given by:
MED = (0+1+0+0+0+0+1+0) / 8 = 0.25
NMED = MED / 3 = 0.083
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Figure 4 : MLAFA2 schematic diagram
Table 3 : MLAFA1 truth table

## Slide 13
Figure 5 : EFA schematic diagram
Table 4 : Comparison of 1 – bit MLAFAs
Types | ML | INV | Dsum (in ps) | Dcout (in ps) | NMED | MAE
EFA | 3 | 2 | 180 | 95 | 0 | 0
MLAFA1 | 1 | 1 | 82 | 60 | 0.083 | 1
MLAFA2 | 1 | 1 | 78 | 0 | 0.083 | 1

## Slide 14: 2 – Bit MLAFA
Figure 6.(a) : MLAFA11
Figure 6.(b) : MLAFA22

## Slide 15
Figure 6.(c) : MLAFA11
Figure 6.(d) : MLAFA21

## Slide 16
Proposed 2 – bit MLAFA from truth table reduction
For two operands A and B, there are four possible combinations. Under an assumed Gaussian distribution for image processing, A = 00 or B = 00 and A = 11 or B = 11 are not considered to ensure a low complexity by using a truth table. The reduced truth table is shown in the Table 5. The exact expressions for the outputs in these eight cases are given as:
Cout = M(A1, B1, Cin)
S0 = M(M(~A0, B0, Cin), M(A0, ~B0, Cin), ~Cin)
= M(M(A1, B0, Cin), M(A0, B1, Cin), ~Cin)
S1 = ~Cout
This design is hereafter referred to as MLAFA33
A1 | A0 | B1 | B0 | Cin | Cout | S1 | S0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Table 5 : Reduced truth table of 2-bit MLAFA

## Slide 17
Figure 6.(e) : MLAFA33 schematic diagram
Table 6 : Comparison of 2-bit MLAFAs
Types | ML | INV | Dsum (in ps) | Dcarry (in ps) | NMED | MAE
MLAFA11 | 2 | 2 | 82 | 21 | 0.107 | 3
MLAFA22 | 2 | 1 | 52 | 0 | 0.107 | 3
MLAFA12 | 2 | 1 | 80 | 43 | 0.089 | 2
MLAFA21 | 2 | 2 | 47 | 32 | 0.089 | 2
MLAFA33 | 4 | 2 | 160 | 30 | 0.080 | 2

## Slide 18: 4 – Bit MLAFA
Figure 7.(a) : MLAFA1212
Figure 7.(b) : MLAFA2121

## Slide 19
Figure 7.(c) : MLAFA2112
Figure 7.(d) : MLAFA1221

## Slide 20
Figure 7.(e) : MLAFA2112
Figure 7.(f) : MLAFA2133

## Slide 21
Table 7 : Comparison of 4-bit MLAFAs
Types | ML | INV | Dsum (in ps) | Dcarry (in ps) | NMED | MAE
MLAFA1212 | 4 | 2 | 286 | 172 | 0.091 | 10
MLAFA2121 | 4 | 3 | 189 | 171 | 0.092 | 10
MLAFA2112 | 4 | 3 | 284 | 172 | 0.092 | 10
MLAFA1221 | 4 | 2 | 181 | 172 | 0.175 | 10
MLAFA1233 | 6 | 2 | 334 | 234 | 0.083 | 9
MLAFA2133 | 6 | 3 | 334 | 234 | 0.081 | 10

## Slide 22: 8 – Bit MLAFA
Figure 8.(a) : MLAFA1212-1212

## Slide 23
Figure 8.(b) : MLAFA2121-1212

## Slide 24
Figure 8.(c) : MLAFA1212-1233

## Slide 25
Figure 8.(d) : MLAFA1212-3333

## Slide 26
Figure 8.(e) : MLAFA1233-3333

## Slide 27
Figure 8.(f) : MLAFA3333-3333

## Slide 28
Table 8 : Comparison of 8-bit MLAFAs
Types | ML | INV | Dsum (in ps) | Dcarry (in ps) | NMED | MAE
MLAFA1212-1212 | 8 | 4 | 460 | 360 | 0.090 | 170
MLAFA2121-1212 | 8 | 5 | 420 | 410 | 0.091 | 170
MLAFA1212-1233 | 10 | 4 | 410 | 130 | 0.082 | 149
MLAFA1212-3333 | 12 | 4 | 600 | 520 | 0.081 | 145
MLAFA1233-3333 | 14 | 4 | 680 | 580 | 0.080 | 169
MLAFA3333-3333 | 16 | 5 | 710 | 600 | 0.080 | 170

## Slide 29
Table 9 : Image processing result of 8-bit MLAFAs
Types | SSIM | PSNR(dB)
MLAFA1212-1212 | 0.2843 | 11.8691
MLAFA2121-1212 | 0.2819 | 11.8280
MLAFA1212-1233 | 0.7124 | 18.7737
MLAFA1212-3333 | 0.7987 | 20.5093
MLAFA1233-3333 | 0.8063 | 20.9441
MLAFA3333-3333 | 0.8166 | 21.8243
(a)
(b)
(c)
(d)
(e)
(f)
(g)
Figure 9 : Image processing result of 8-bit MLAFAs : (a) Original, (b) MLAFA1212-1212, (c) MLAFA2121-1212, (d) MLAFA1212-1233, (e) MLAFA1212-3333, (f) MLAFA1233-3333, (g) MLAFA3333-3333

## Slide 30: IMPLEMENTATION (II. Approximate Compressor)

## Slide 31: 4:2 MLAC
Figure 10.(a) : MLAC1 schematic diagram
Figure 10.(b) : MLAC2 schematic diagram

## Slide 32
Figure 10.(c) : MLAC22-1 schematic diagram
Figure 10.(d) : MLAC22-2 schematic diagram

## Slide 33
Figure 10.(e) : MLAC12-1 schematic diagram
Figure 10.(f) : MLAC12-2 schematic diagram

## Slide 34
Figure 10.(h) : EC schematic diagram
Figure 10.(g) : MLAC21 schematic diagram

## Slide 35
Proposed MLAC based on K-Map simplification
To further decrease the hardware complexity, an additional MLAC, namely MLAC4, is proposed; this circuit uses 2 outputs (rather than 3) for the final result.
The design of this MLAC is accomplished as per the following 3-step process:
  Step 1: Approximation on the number of outputs. Use 2 outputs to denote the results so the binary 11 is employed to represent results larger than 11.
  Step 2: Approximation of the expression for the K-map in Step 1. Depending on the properties of the majority logic, simplified equations can be found by introducing few errors.
  Step 3: Computing the error distance by combining Step 1 and Step 2.
From the simplified K-Map, we can write:
Carry = M(M(P3, P2, P1), M(P5, P4, 1), 1)
Sum = M(M(P3, P2, P1), P5, P4)
Table 11 : K-Map of proposed MLAC4 after step 2
Table 10 : K-Map of proposed MLAC4 after step 1

## Slide 36
Table 12 : Comparison of 4:2 MLACs
Types | ML | INV | Dsum (in ps) | Dcarry (in ps) | NMED | MAE
EC | 6 | 4 | 378 | 317 | 0 | 0
MLAC1 | 2 | 2 | 211 | 0 | 0.1 | 2
MLAC2 | 2 | 2 | 181 | 163 | 0.075 | 1
MLAC22-1 | 2 | 2 | 184 | 0 | 0.1 | 2
MLAC22-2 | 2 | 2 | 212 | 115 | 0.075 | 1
MLAC12-1 | 2 | 2 | 155 | 0 | 0.075 | 1
MLAC12-2 | 2 | 1 | 154 | 99 | 0.1 | 2
MLAC21 | 2 | 2 | 214 | 196 | 0.1 | 2
MLAC4 | 4 | 0 | 179 | 174 | 0.087 | 3
Figure 10.(i) : MLAC4 schematic diagram

## Slide 37: IMPLEMENTATION (III. Approximate Multiplier)

## Slide 38
Figure 11 : Proposed design flow of n x n MLAMs

## Slide 39: Partial Product Generation
For a 2 x 2 MLAM, let the multiplicand be A1A0 and the multiplier be B1B0.
Out0 = M(A0, B0, 0)
Out1 = M(A0, B1, 0)
Out2 = M(A1, B1, 0)
∆ = M(A1, B0, 0)
where Out0, Out1, Out2 are the partial products (PP) and ∆ represents a compliment bit
Figure 12 : 2x2 MLAM PP generation schematic diagram

## Slide 40
Figure 14 : 8x8 MLAM PP generation schematic diagram
Figure 13 : 4x4 MLAM PP generation schematic diagram

## Slide 41
Figure 15 : 4x4 MLAM PP and complement bit generation

## Slide 42
Figure 16 : 8x8 MLAM PP and complement bit generation schematic diagram

## Slide 43: Complement Bit Selection
Too many compensation bits will lead to a larger overhead when calculating the subsequent compression; however, too few compensation bits will cause the final result to lose accuracy. Therefore, a tradeoff must be assessed when selecting an appropriate number of compensation bits.
When selecting the compensation bits and to control the error within a reasonable bound, the compensation bits for the lowest weight are ignored.
To measure the importance of each complement bit as well as to determine the ignored items, an influence factor denoted by is defined; this is required to show the impact of a complement bit on the final NMED. For an n x n MLAM, it can be expressed as follows:
where 2i denotes the weight of the complement bit; n denotes the size of the multiplier; N denotes the number of cases that the output (∆) is 1 when traversing all possible cases (as a function of n). Only when the inputs are both 1, ∆ is effective (and equal to 1). Except the two inputs of ∆, there are possible cases for the inputs of multipliers.

## Slide 44
The influence factor has the following properties:

## Slide 45
Assuming that the number of ignored compensation bits is p; as of different complement bits are mutually independent and linearly superposed, the NMED of a n x n approximate multiplier is given by:
Similar to the above analysis, the expression for MAE can be found. Another influence factor denoted by EC2ix is defined; this is required to show the impact of a complement bit on the final MAE. For an n x n MLAM, it can be expressed as follows:
The MAE of a n x n approximate multiplier is given by:
Table 12 : Value of Influence Factor when n = 4 and n = 8

## Slide 46
Figure 18 : Complement bit selection (MAE versus p): (a) 4 x 4 MLAM, and (b) 8 x 8 MLAM2x2
Figure 17: Complement bit selection (NMED versus p): (a) 4 x 4 MLAM, and (b) 8 x 8 MLAM

## Slide 47: 4 x 4 MLAM
Figure 20 : 4x4 MLAM-EC (p=1) schematic diagram
Figure 19 : 4x4 MLAM-EC (p=1) PPR circuitry

## Slide 48
Figure 22 : 4x4 MLAM-AC2 (p=1) schematic diagram
Figure 21 : 4x4 MLAM-AC2 (p=1) PPR circuitry

## Slide 49
Figure 24 : 4x4 MLAM-AC2 (p=4) schematic diagram
Figure 23 : 4x4 MLAM-AC2 (p=4) PPR circuitry

## Slide 50
Types | ML | INV | Delay (in ps) | NMED | MAE
4x4 MLAM-EC (p=1) | 39 | 16 | 1140 | 2.22 | 2
4x4 MLAM-AC2 (p=1) MLAC22-2 | 33 | 13 | 1024 | 14.44 | 12
4x4 MLAM-AC2 (p=4) | 24 | 9 | 812 | 61.59 | 66
Table 13 : Comparison of 4x4 MLAMs

## Slide 51: 8 x 8 MLAM
Figure 25 : MLAM1_8X8_p1 [8x8 MLAM using 4x4 and exact PPR] schematic diagram

## Slide 52
Figure 25 : MLAM1_8X8_p1 PPR circuitry

## Slide 53
Figure 27 : 8x8 MLAM (p=10) (using 2x2 MLAM and exact PPR) schematic diagram

## Slide 54
Figure 28 : 8x8 MLAM (p=10) (using 2x2 MLAM) PPR circuitry

## Slide 55
Figure 29 : MLAM3_8X8_p10_MLAC4 [8x8 MLAM using 2x2 and approximate PPR] schematic diagram

## Slide 56
Figure 30 :Approximate PPR circuitry design for 8 x 8 MLAMs: (a) MLAC (2 outputs) based (p = 10), and (b) MLAC (3 outputs) based (p = 10).

## Slide 57
Types | ML | INV | Delay (in ps) | NMED | MAE
MLAM1_8x8_p1 | 189 | 90 | 3184 | 0.0131 | 3468
MLAM2_8x8_p1 | 173 | 82 | 3082 | 0.0191 | 6572
MLAM3_8x8_p10_MLAC4 | 120 | 36 | 2475 | 0.0267 | 9120
MLAM4_8x8_p10_MLAC22-2 | 116 | 52 | 2228 | 0.0318 | 9476
MLAM5_8x8_p10_MLAC12-1 | 116 | 52 | 2171 | 0.0346 | 9820
Table 13 : Comparison of 8x8 MLAMs

## Slide 58
Types | SSIM | PSNR(dB)
MLAM5_8x8_p10 | 0.8568 | 14.5279
MLAM4_8x8_p10 | 0.9441 | 22.0034
MLAM3_8x8_p10 | 0.9532 | 25.5093
MLAM2_8x8_p1 | 0.9611 | 30.3539
MLAM1_8x8_p1 | 0.9705 | 36.6246
Table 14 : Image processing result of 8x8 MLAMs
Figure 31 : Image processing result of 8-bit MLAFAs : (a) Original, (b) MLAM5_8x8_p10, (c) MLAM4_8x8_p10, (d) MLAM3_8x8_p10, (e) MLAM2_8x8_p1, (f) MLAM1_8x8_p1

## Slide 59: Epilogue
This paper has presented a design, analysis and evaluation of majority logic based approximate adders and approximate multipliers. The following conclusions can be drawn:
By combining the proposed 1-bit MLAFA and the existing 1-bit MLAFA, multi-bit MLAFAs can be designed with a relatively large error. The proposed MLAFA33 designed by truth table reduction can provide the solution for improving accuracy. For 8-bit adders, MLAFA1212-1233 (with a reduction of 58 percent in majority gates as well as 50 percent in delay) and MLAFA1212-3333 (with a reduction of 50 percent in majority gates as well as 50 percent in delay) are superior to other designs.
Based on the proposed 2 x 2 MLAM, we can selectively design multi-bit multipliers by adding the complement bits. From the presented theoretical analysis, for a 4 x 4 multiplier, when p changes from 3 to 4, the NMED increases sharply; for an 8 x 8 multiplier, when p is smaller than 10, the NMED increases slowly but when p is larger than 10, the NMED increases rapidly. So p = 3 and p = 10 are the best choices for the 4 x 4 multiplier and the 8 x 8 multiplier, respectively.
MLAC22-2 and MLAC12-1 show the best overall performance among these MLACs based on MLAFAs. Compared with the exact design, the proposed designs save 67 percent of majority gates, 50 percent of inverters, 50 percent of delay and 67 percent of carry chain. Although MLAC4 requires two additional 3-input majority gates, MLAC4 only has 2 outputs, which is likely to reduce the approximate operation in the PPR circuitry. The MLAC4 based 8 x 8 multiplier using 2 x 2 multipliers (p = 10) reduces the number of majority gates by up to 48 percent, the number of inverters by up to 67 percent, and the delay by up to 47 percent compared to the exact counterpart, achieving a significant decrease of hardware without incurring in large errors.

## Slide 60: References
C. Labrado, H. Thapliyal and F. Lombardi, "Design of majority logic based approximate arithmetic circuits", Proc. IEEE Int. Symp. Circuits Syst., pp. 2122-2125, 2017.
S. Angizi, H. Jiang, R. F. DeMara, J. Han and D. Fan, "Majority-based spin-CMOS primitives for approximate computing", IEEE Trans. Nanotechnol., vol. 17, no. 4, pp. 795-806, Jul. 2018.
C. Chang, J. Gu and M. Zhang, "Ultra low-voltage low-power CMOS 4–2 and 5-2 compressors for fast arithmetic circuits", IEEE Trans. Circuits Syst. I, vol. 51, no. 10, pp. 1985-1997, Oct. 2004.
H. Cho and E. E. Swartzlander, "Adder and multiplier designs in quantum dot cellular automata", IEEE Trans. Comput., vol. 58, no. 6, pp. 721-727, Jun. 2009.
V. Pudi and K. Sridharan, "Low complexity design of ripple carry and Brent-Kung adders in QCA", IEEE Trans. Nanotechnol., vol. 11, no. 1, pp. 105-119, Jan. 2012.
S. Mittal, "A survey of techniques for approximate computing", ACM Comput. Surv., vol. 48, no. 4, 2016.
S. L. Eddins and M. T. Orchard, "Using MATLAB and C in an image processing lab course", Proc. First Int. Conf. Image Process., vol. 1, pp. 515-519, 1994.

## Slide 61: Thank you